## Slide 1: Note for the trainer (1/2)
This training can be carried out ’Live’ or as a trainer-led online training event. For online training the following tools could be used: Mentimeter, Slido, Padlet, Jamboard, (collaborative digital whiteboard).
The training should be interactive – with the aim that participants will actively contribute and learn both from you and each others’ experience. Interactive elements are marked with the symbol at the right.
Some slides contain notes with additional explanation and/or extra material to read. The Instructions to trainer contain guidance and tips for using the slide.
You can decide to hide/add slides to fit your presentation and adapt to the context.
You will find all information about the training in the Training Unit Information (duration, target group, goal, etc).

## Slide 2: Note for the trainer (2/2)
This unit will be of interest not only to Trusted Partners, but also to energy auditors, energy experts, and local energy advisors.
Do not forget to fill out the Template Monitoring Training and to ask participants for feedback with the prepared form (included in the document Template Monitoring Training).
Ideally, participants prepare for this unit with the exercise below.
Before giving this training, ask the participants to think about the following two questions. It will serve as a discussion starting point for the unit:
examples of Energy Efficiency measures that have been implemented by companies, think of the main arguments why the investment decision was successful
and other Energy Efficiency measures that failed to be implemented, think of the main reasons.

## Slide 3: Note for the trainer – glossary of terms
EE Energy Efficiency
TP Trusted Partner
ESS Energy Service Supplier
MB Multiple Benefits
NEB Non-Energy Benefit
EEM Energy Efficiency Measure

## Slide 4: Multiple Benefits Unit II How to integrate Multiple Benefits in the company‘s strategy
Date
Organisers
Notes: Target group for the training: TP and ESS addressing mainly manufacturing industries
Goals: Understand how the decision making process works in KMUs and how to integrate the Multiple Benefits (including monetarization part)
Duration: 2-3 hours

## Slide 5: Who are we?
Insert your own picture and contact info
Notes: Instructions to trainer: Use this slide (or a similar one) to introduce yourself/selves to the group, AND to let the participants introduce themselves to each other in a “round-the-table”.
Start with presenting yourself/selves: Who are you? What is your role and experience from working with Energy Efficiency in SMEs? With networking and collective approaches?
Summarize after the round table introduction.
Find out (best before the training) if they have a TP or ESS role. While Unit 1 of this training will be of interest to both groups, we expect that Unit 2 is mainly interesting for ESS or for Energy Managers within larger SMEs.
Before getting started, we will start an introducing round. Each participant could start with answering these questions:
Who are you? (Name, organisation)
What is your experience from supporting/interacting with SMEs? (Energy related or not!)
What do you expect from this training?

## Slide 6: Content
Unit I
Introduction to Multiple Benefits
Unit II
How to integrate MB in the company‘s strategy

## Slide 7: Goals of unit II
You find arguments to link Energy Efficiency measures to the core business of a company
You know the three parameters of a strategic investment
You understand how to gather Non-Energy Benefits at process and company level
You can apply the strategic analysis to concrete examples
You know the different financial indicators and their limits

## Slide 8: Key elements Unit I
Notes: Instructions to trainer: You can start here by asking who participated in the first unit, if the units were organized separately.

## Slide 9: Definition of Multiple Benefits
Energy Benefits: energy and energy cost savings
Non-Energy Benefits (NEBs): Any kind of positive environmental, economic or social effects on all business areas of a company that can occur in addition to the energy benefits
= other beneficial effects
Notes: Instructions to trainer: Start with a definition of Multiple Benefits
We will discuss Multiple Benefits of Energy Efficiency or of an Energy Efficiency measure in particular.
Multiple Benefits have two components: energy benefits and non- energy benefits

## Slide 10: Take-aways
An Energy Efficiency Measure can often have additional positive effects on the production, the operation & maintenance, the work environment or the environment or on the brand image.
The Non-Energy Benefits (NEBs) are often overlooked in decision process.
NEBs can be used to get internal support to implement an EEM (well-targeted communication)
Some NEBs are easy to quantify/monetize whereas others are almost impossible
Non-monetizable NEBs can contribute to a positive decision in the investment process
Notes: If participants should take away a few elements from Unit I, it would be …

## Slide 11: Unit II: How to integrate MB in the company‘s strategy?

## Slide 12: Discussion
  Give an example of Energy Efficiency measure that has been implemented by a company, think of the main arguments why the investment decision was successful
  Give an example of an Energy Efficiency measure that failed to be implemented, think of the main reasons
Notes: Instructions to trainer: Start this second unit with a discussion among the participants. You could give them the two topics as “homework” before the training, it is easier if they had some time to think about it. Otherwise, allow 5 min for all participants to think about it.
Try to figure out if the energy measures improved the process in a way, or were seen as strategical by the company. Or were other Non-Energy Benefits mentioned? How was the collaboration between different organizational roles (e.g., production manager, technical manager, sustainability manager, external advisors, etc.)?
Allow approx. 10 min for the discussion.

## Slide 13: Problem
The ‘kWh approach‘ is not sufficient. Process and strategic considerations need to be taken into account for EEM to be prioritized
Energy people and process/production people, but also top-management people, are not speaking the ‘same language‘
Notes: Instructions to trainer: Hopefully, thanks to the discussion, you will have discussed that only the “kWh approach” and financial approach is not enough.
In this unit we will go deeper into the process and strategic analysis and see how it is possible to bridge the gap between energy, process and strategy people. This finding is part from the MBenefits Project.

## Slide 14: Multiple Benefits approach
Source: https://www.mbenefits.eu/
Notes: Instructions to trainer:
The elements (methods and examples) presented in this training are issued from the MBenefits project.
Source: https://www.mbenefits.eu/
The MBenefits approach or methodology identifies 5 steps to help enterprises and energy service suppliers to take NEBs in account and lead to a positive investment decision for EEMs.
For more details about the five steps, all material of the project is available online, such as webinar in German, Polish and Italian.

## Slide 15: Steps to the Multiple Benefits analysis
1. EEM level
2.production level
3. company level
Identify advantages at:
Notes: Instructions to trainer: In this unit we decided to provide more detail on how to identify the NEBs. The steps are detailed in the next slides.

## Slide 16: 1. Identify MB at EEM level
directly linked to the EEM
  Energy, costs and CO2 reduction
  maintenance reduction
Generally from the energy audit (energy people)
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
Notes: Firstly, MB directly linked to the EEM should be identified, these will be found in the energy audit as a result from the energy service supplier („energy people“). In some cases reduction in maintenance might be already included in the audit.

## Slide 17: 2. Identify MB at process level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
Process people realize a process mapping of the operations
Notes: As a second step, it is necessary to analyse the process(es).
A definition of a process is: Process is a sequence of operations connected to each other, producing results.
The process mapping consists of identifying all steps forming the process in a chart. Defined boundaries are necessary (process supplier / customer). The process customer can be an internal customer (the next process in the value chain) or the final buyer of the product or service.
The process mapping should be realized by production people, best in collaboration with energy people.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 18: 2. Identify MB at process level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
Analyse the source of its operational effectiveness (safety, quality, cost, time-to-market)
Analyse of critical-to-quality parameters (CTQ)
Notes: Once the process is mapped, its operational effectiveness (OE) can be analysed. OE means performing similar activities better than rivals, reducing defects in products or developing better products faster. OE ist composed of four interrelated dimensions:
Safety (of staff)
Quality (of products and processes)
Costs (borne to produce a company‘s value proposition)
Some examples for indicators in the next slide.
Critical-to-quality parameters are parameters which, if they are not met, will imply that the customer will not be satisfied or the process not accomplished properly. CTQ Parameters are measurable and can be improved by EEMs.
Source: D4.2 Training Tools – Mbenefits : https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)
An example for CTQ parameters could be:
If the customer says „I want a very good fruit salad“, the relevant factors would be: Taste, Temperatur and quantity.
THE CTQ parameters could be: Taste: fruit-mix; sweet/not too sweet
Temperature: not cold, but < 15°C
Quantity: > 200 g
Example from: Webinar Serie 'Erfolgreich am Markt durch Energieeffizienz' Teil 3, available at:https://www.youtube.com/watch?v=Qm9hXMHBqgw (last accessed 16.11.2021)

## Slide 19: Operational excellence indicators
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
Safety
number of accidents per year
number of days of absence per year perception of safety by the staff (annual survey)
percentage of employees trained in good practices
Quality
Downtime per day
Percentage of products conforming to specifications
Percentage of raw material losses
Throughput (quantity per unit time)
Cost
costs of raw materials per month/year
costs of raw materials losses per month/year
cost of energy, gas, water per month/year
cost of additional hour of line operators
Time-to-market
preparation time per day
production time per day
machine downtime per day
number of delivery problems per year
number of new products developed per year
Notes: Instructions to trainer: Go through the indicators safety, quality and time-to-market. The costs indicators are pretty straightforward.
These indicators will enable to quantify and if possible monetize the NEBs. They are with more or less efforts measurable and possible to quantify with production people. They should be included in the strategic analysis Value- cost- risk (step 3)
These quality indicators illustrate the fact that the concept of quality not only includes product quality but also the quality of the production process, evaluated by its ability to provide products that meet quality requirements, as well as by its reliability (measured by the percentage of operation without failure) and flexibility (process ability to respond very quickly to changes in demand).
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 20: 2. Identify MB at process level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
  Focus on energy services instead of machines and energy carriers
    lighting, ventilation, air conditioning, cooling & refrigeration, heating, hot water, automated processing of information & communication, motive power (engines)
  It bridges the gap between process people and energy people
Notes: Still in the second phase (identify advantages at the production level), another step is to look for energy services.
Energy services are: lighting, ventilation, air conditioning, cooling & refrigeration, heating, hot water, automated processing of information & communication, motive power (engines).
They make the link between operational excellence and energy consumption. It‘s the common ground that energy people and process people can work on.
Often process people are not sufficiently competent to evaluate the quality and security of the energy services feeding the value chain and energy specialists focus on machines and energy carriers. This analysis requires multidisciplinary competences.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 21: 2. Identify MB at process level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
How?
  Focus on energy services instead of machines and energy carriers
Source: Part of the presentation from U.S DOE, Quantifying the Additional Benefits from Energy Efficiency, 12.01.2020 (Cooremans)
Notes: Instruction to trainer: Use this slide to illustrate the link between energy carriers / equipment, energy services and processes. Show with the column „responsible“ again who is „in charge“ for realizing the analysis.
The traditional approach should be reversed and enlarged, not focusing on machines, equipment and energy carriers but should
first understand the process
Identify the key energy services, analyse their related risks and constraints
look for ways to improve energy services quality and reliability.
Analyse machines and equipements which produce these energy services.
Identify EEMs that contribute to quality and reliability of energy services and reduce the energy consumption of machines and equipment at the same time.

## Slide 22: 2. Identify MB at process level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
When focusing on energy services, energy people and process people should look for:
Key energy services (risks, constraints?)
How to improve energy services quality and relability
Machines and equipment producing these energy services
Identify EEMs that contribute to quality and reliability of energy services and reduce the energy consumption of machines and equipment at the same time
Notes: Instruction to trainer: Use this slide as „recap“, when working at the process level.
There are some questions to be answered for each process:
what are the goals of the process (defined to meet the expectations of the process customer)?
What are the process key factors of success (production conditions)?
What are the risks attached to the process?
What is the value contribution of each energy service to each substep?
For instance, in an example of Novelis, an aluminium foil company: concerning lighting, a minimum of 300 lux is necessary in the production area of the factory and a minimum of 200 lux in the storage area; for high-to-medium temperature heat, minimum and maximum levels are necessary to ensure product quality; for compressed air, a certain level of humidity is required for quality reasons.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 23: 3. Identify MB at company level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
  Categorize MB in strategic terms
  Investment (and EEM) will be seen as strategic if it contributes to the competitive advantage of the company
  based on three parameters:
    Value proposition
    Cost
    Risk
Notes: This step is dedicated to assess the contribution of EEMs to the strategic direction of a company. It is important to obtain top-management support. The strategic character is more influential than profitability in companies’ investment decision-making.
An investment will be considered strategic if it contributes to create, maintain or develop a sustainable competitive advantage. Which means reducing costs, reducing risks and increasing the value proposition.
Once NEBs of each identified EEM are determined, you need to categorize them in strategic terms, which means their contribution to risk reduction, cost reduction and increase of value proposition.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 24: 3. Identify MB at company level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
Value
Costs
Risks
Value proposition developed by a firm for its customers/customer segments
Risks to create and deliver the value proposition
Operations and administrative costs to create and deliver the value proposition
Source: Cooremans (2011)
Notes: Instruction to trainer: Describe more precisely all 3 components of the competitive advantage
The value proposition is a value of use and no monetary value. It’s the benefits the customer get when using the service / product. Increasing the value proposition (thanks to EEMs) will make more customer buy the product for example and it will turn in additional income.
Cost: bourne to conceive and produce the value proposition. EEMs can reduce many costs, beyond energy costs.
Risk: A reduction of risk exposure often conducts to a value proposition increase and cost decrease. For example: More consistent quality positively contributes to the value proposition and turnover, while reduction of raw material losses translates in cost reduction. Investment in energy savings technologies have potential negative risks for companies (technical risks related to technologies reliability, resources risks (change of suppliers or information systems), human errors risks (lack of skills in the use or maintenance of new equipment), and risks of production or information processes dysfunctions in case of replacement of existing equipment. Another risk of energy-efficiency investments is related to the uncertainty of their outcome, as energy savings and financial savings resulting from these investments are uncertain). However, although they are mentioned in the literature, these risks are rarely mentioned by companies as a barrier to energy-efficiency investments.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 25: 3. Identify MB at company level
Identify advantages at EEM level
Identify advantages at production level
Identify advantages at company level
  Example of Value Proposition:
  Supermarket chain: Provide a great shopping experience that meets consumers’ changing needs and builds loyalty
  Furniture maker: High-quality, custom-made furniture
Notes: Instruction to trainer: The goal of this training is not to define the value proposition of a company. Here are 2 examples. Often the value proposition can be read on the website of the enterprise. You could ask participants to reflect on this more.
It is of importance for an Energy Service Supplier to have the value proposition of an SME in mind when taking a look at the NEBs.
To determine the customers segments and the value proposition, the business model Canva is very useful. More information and download link for Canva is available on this website for example: https://www.businessmodelsinc.com/about-bmi/tools/business-model-canvas/.
Examples from MBenefits case studies.

## Slide 26: Link between Energy Efficiency measure and competitive advantage
Example 1: Industrial bakery
Quality is top priority
Always developing new products
Production runs 24 hours a day, seven days a week, in shifts. More than 30.000 rolls per hour.
Every product meets its specifications exactly.
Source: www.fortisa.ch
Notes: Instruction to trainer: with the following example, you will get participants involved in trying to assign the NEBs to one component of the competitive advantage. Start with presenting the context of the case study.
Source: D4.2 Training Tools – Mbenefits : https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 27: Link between Energy Efficiency measure and competitive advantage
  EEM (from the energy audit)
  Replacement of the bake ovens
  Lighting improvement
  Hot water usage
  Insulation of pipes
  Recalibration of thermostat
  Would save 6,5% of the energy bill
Example 1: Industrial bakery
Notes: Instruction to trainer: Continue with presenting the proposed EEMs from the energy audit.
“An example of Value-Cost-Risk analysis is given in Figure 9, based on the information given by Kannan and Boie (2002): an energy audit analyses a bakery process lines in the production unit to determine “which amounts of energy were consumed during a reference period and how this energy was used” (Kannan and Boie 2002:948). The audit recommends several energy-saving measures: replacement of the bake ovens, lighting improvement, hot water usage, insulation of pipes, and recalibration of thermostat. These measures could save about 6.5 percent of the total energy bill. “
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 28: Link between Energy Efficiency measure and competitive advantage
  EEM (from the energy audit)
  Replacement of the bake ovens
  Lighting improvement
  Hot water usage
  Insulation of pipes
  Recalibration of thermostat
Example 1: Industrial bakery
  → better heating quality of the new ovens
  → shorter preheating time of the ovens
  → better oven and pipe insulation
Notes: Instruction to trainer: from the EEMs, we can deduce some NEBs, which should help participants to find more, related to the core business.
The audit does not mention any Non-Energy Benefits but, based on the description given by Kannan and Boie (2002), we can hypothesize the following NEBs of the energy-saving measures described.
Source: D4.2 Training Tools – Mbenefits : https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 29: Find how the EEMs contribute to the competitive advantage
  EEM (from the energy audit)
  Replacement of the bake ovens
  Lighting improvement
  Hot water usage
  Insulation of pipes
  Recalibration of thermostat
Example 1: Industrial bakery
  → better heating quality of the new ovens
  → shorter preheating time of the ovens
  → better oven and pipe insulation
Value
Costs
Risks
Notes: Instruction to trainer: Ask the participants to categorize and translate these NEBs in costs and risks reduction and value proposition increase. In a face-to-face workshop, you can hand out an MB list to participants to help them (see Unit 1).
You can mark on a board with post-it ideas from participants or use an online tool.
You can guide the participants:
what could be the influence of a better heating quality for such a precision manufacturing process => should lead to increased product quality and reliability => this has impact on the value proposition, may influence higher sales.
what could be the influence of a shorter preheating time, which means less time for a production cycle => increased throughput and productivity => will reduce costs
what could be the influence of better oven and pipe insulation, think about the workplace and employees => increased workplace comfort and safety. This can be turned in costs reduction (may reduce insurance premiums ; encourages higher employee productivity and loyalty) and also in risk reduction (reduce risk of accident).
Influence on changing old equipment => reduce equipment breakdown
Directly linked to energy consumption, reduced energy bills. Reducing energy consumption, which means CO2 emissions are reduced as well, together with possible legal and commercial risk. Also, reduced maintenance.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 30: Find out how the EEMs contribute to the competitive advantage
  Improved product quality
  Improved product reliability
  Reduced workplace accident risk
  Reduced commercial risk
  Reduce carbon risk
  Reduce equipment breakdown
  Increased workforce productivity (thanks to increased comfort)
  Reduced production time (thanks to reduced oven preheating time)
  Reduced product loss (thanks to better heating quality of the oven)
  Reduced insurance premiums
  Reduces CO2 costs
  Reduced maintenance costs
  Reduced energy costs
Example 1: Industrial bakery
Value
Costs
Risks
Notes: Instruction to trainer: Once all participants have given their ideas, and these have been attributed to one component, show the ‚results‘ of what has been found in the case study.
If adopted, energy performance measures would thus significantly contribute to the three dimensions of the bakery’s competitive advantage: increased value (better product quality and reliability), reduced costs (higher productivity of ovens and employees, reduced product loss, reduced insurance premiums and maintenance cost), and reduced risks (increased workplace safety). Better product quality and reliability may be a source of higher sales.
The figure shows how the three dimensions of competitive advantage are linked. For instance, reduction of the accident risk leads to a cost reduction, a better product quality leads not only to additional sales but also to lower product loss.
Source: D4.2 Training Tools – Mbenefits: https://www.mbenefits.eu/static/media/uploads/site-6/library/Deliverables/d4.3_training_tools.pdf (last accessed 15.11.2021)

## Slide 31
Source: Cooremans Presentation TNO workshops – January 2021
Example 1: Industrial bakery
Notes: Instruction to trainer: This is another way of illustrating the arguments and NEBs with the process mapping.

## Slide 32: Examples

## Slide 33: New batteries with modern chargers to save time, reduce cost at warehouse operation
Example #1
Impacts on operations
Security
Better management of batteries for pallet trucks
Optimize operation of warehouse (space savings).
Quality
Improve life cycle of batteries.
Impact on costs
Reduction of energy and maintenance costs
Impact on time
Improved time management during charging and due to
Employee scheduling
Source: Case Study Mbenefits, https://www.mbenefits.eu/news-resources/library/
Notes: Instruction to trainer: choose one of the examples, first go through the context of the case study, then through the impacts on the operations (here it is to link with the parameters of the operational excellence). Go through the strategic analysis.
Source: Case Study Mbenefits, available at: https://www.mbenefits.eu/news-resources/library/(last accessed 9.11.2021)
Introduction
Alfa-Beta (AB) Vassilopoulos S.A. is a supermarket chain based in Greece. Their value proposition is to provide a great shopping experience
that meets consumers’ changing needs and builds loyalty, all provided with 24-hour technical support.
They aim to inspire customers to make healthier choices, increase product transparency, and eliminate waste. Part of AB Vassilopoulo’s
goal is to target smarter and more efficient operations. Given the staff’s time constraints and the fact that an energy audit
was not legally required at the warehouse in focus, participating in the Multiple Benefits project offered a unique opportunity to investigate
energy saving opportunities and additional benefits.
Energy insights -2,6% reduction of energy demand
Audit identified following measures:
Replace Lead-Acid Batteries with Lithium-Ion Batteries for forklifts
Replace existing chargers with modern chargers designed to provide fast battery charging.

## Slide 34: Rooftop solar, heat exchanger to deliver on Supermarket chain’s sustainability ambitions
Example #2
Impacts on operations
Security
Reduction of energy demand
Quality
Better quality of energy services
Impact on costs
Reduction of energy and maintenance costs
Impact on time
Not impacted
Source: Case Study Mbenefits, https://www.mbenefits.eu/news-resources/library/
Notes: Instruction to trainer: Choose one of the examples, first go through the context of the case study, then through the impacts on the operations (here it is to link with the parameters of the operational excellence). Go through the strategic analysis.
Source: Case Study Mbenefits, available at: https://www.mbenefits.eu/news-resources/library/ (last accessed 9.11.2021)
Introduction
Alfa-Beta (AB) Vassilopoulos S.A. is a supermarket chain based in Greece. Their value proposition is to provide a great shopping experience that meets consumers’ changing needs and builds loyalty, all provided with 24-hour technical support. They aim to inspire customers to make healthier choices, increase product transparency, and eliminate waste. Part of AB Vassilopoulo’s goal is to target smarter and more efficient operations. Given the staff’s time constraints and the fact that an energy audit was not legally required at the warehouse in focus, participating in the Multiple Benefits project offered a unique opportunity to investigate energy saving opportunities and additional benefits.

## Slide 35: Financial background
Notes: Instruction to trainer: Emphasize again on the fact that monetarization is not the only important parameter!! This short part concerning the financial background serves as introduction for the indicator used in the case studies. You can also choose to skip this part.
Strategic analysis is a good basis to start a financial assessment, because its three components can have impacts on investment profitability: risk reduction translates into additional turnover or reduced costs; improved value proposition would translate into additional turnover to improve long-term profitability together with cost reduction.
Also as seen before NEBs linked with operational excellence parameters can be easy to quantify.
Some NEBs are easy to monetize (increased production, higher productivity, reduced dowtime, reduced waste or wastewater etc), some of them are easy to quantify but maybe harder to monetize (reduced noise, better air quality, improved staff satisfaction).
Nevertheless, only monetary aspects are not enough to push investment decisions and that‘s why it is crucial to list all potential benefits of an Energy Efficiency measure (EEM), even if it‘s not possible to translate them into numbers, to:
find the right interlocutor in the company who could also push the project (financial, technical, management position) and
also to link the EEM with cost reductions/ lower risks / added value to the company core business.
NEBs can affect how decisions are made, which budget it gets paid from, also when it‘s described qualitatively.

## Slide 36: Parameter for investments
Duration
Initial capital expenditure, also CAPEX in t=0
Expected cashflows (from t=1 to t=T)
Additional capital spending (from t=1 to t=T)
Terminal value (t=T)
Notes: Instruction to trainer: If needed, you can use these slides to do a recap about investments parameters. Relevant for the understanding of the examples are the duration and the CAPEX.
Investment duration = the number of years during which are taken into account the investment flows
CAPEX for long term fixed assets, purchasing or construction value, must include working value at t=0
Cash flows: generally annual, composed of 3 elements: operating earnings after taxes ; additional capital expenditure ; changes in working capital needs
Additional capital expenditure: needed to maintain initial investment in good state or to increase production and sales ; may have influence on terminal value
Terminal value = the selling price of an asset less any removal costs at the end of its life; = market value of equipment or building at the end of investment duration
Source: Catherine Cooremans, TNO Workshop, 19.01.2021

## Slide 37: Cashflows of an investment
t0
t1
t2
time
t3
t
T
Initial outflow
Cash inflow
Cash inflow
In-between additional capital spending
Cash inflow
Final cash inflow
Notes: Instruction to trainer: If needed, you can use these slides to do a recap about investments parameters. Here you can illustrate the initial outflow, cash inflow and final cash flow.

## Slide 38: Time value of money
Present
Future
Compound interest
x Discount factor
r = discount rate
t= investment duration in years
Interest of 7% (present to the future) or discount rate (future to the present of 7% during one year)
1.000
1.000 x 1,07
1.070 / 1,07
1.070
Notes: Instruction to trainer: To illustrate how to account for the time value of money with the discount rate.
*Slide comes with an animation (example with 7% discount rate).
Time value of money means that a sum of money is worth more now than the same sum of money in the future. This is because money can grow only through investing. This is a core principle of finance.
Source : Catherine Cooremans, TNO Workshop, 19.01.2021

## Slide 39: Example of present value with a discount rate of 7%
Present value
100 / 1,07 = 93,46 €
200/ 1,072 =172,42 €
Total =265,88 €
0
1
2
100 €
200 €
year
Notes: Instruction to trainer: To illustrate how to account for the time value of money with the discount rate.
The present value of two cash inflows (100 € and 200 €) made the future is equal to 265,88 €, not 300 €.
Source : Catherine Cooremans, TNO Workshop, 19.01.2021
-----
Example from Multiple Benefits Webinar 3: Finanzanalyse von Energieeffizienz-Projekten, IREES, accessible at : https://www.youtube.com/watch?v=NwAdPB-OjU0 (last accessed 17.11.2021)
If someone wants to give you 1.000 euros in 25 years, you’ll have to renounce to following amounts regarding the discount rate of:
Discount rate 0% : payout 1.000 euros ; renouncement of 0 euros
Discount rate 5% : payout 295 euros ; renouncement of 705 euros
Discount rate 10% : payout 92 euros ; renouncement of 908 euros

## Slide 40: Financial evaluation method
Return of investment (ROI)
Payback method (PP)
Net present value (NPV) – dynamic
  Discount rate
  Duration of investment
Internal rate of return (IRR) - dynamic
PP
Notes: Instruction to trainer: If needed, you can use these slides to do a recap about financial indicators
Source: Catherine Cooremans, TNO Workshop, 19.01.2021
ROI is the amount of money received from your investment, expressed in %. Total profit = (total annual savings – invested capital).
Example: Jo invest 1.000 € in a firm and sold his shares for 1.200 € one year later. Divide net profits (1.200- 1.000) by the investment costs or invested capital (1.000 €) = 20%.
ROI better to avoid, doesn‘t take the timing of cash flows into account, inferior to NPV
Payback method: how fast will the savings pay for the investment
If the cash-flows vary from one year to another, there is no applicable formula to compute the payback.
Doesn‘t take in account the time value of money and only considers the cash inflows until the investment cash outflows are recovered. Cash inflows after the payback time are not part of the analysis.
NPV and IRR are both dynamic methods, which means they take into account the time value of money.
NPV
Net present value is the difference between present value of all inflows less present value of all outflows.
Take in account the discount rate and the investment duration
Selection rule: if NPV is greater than 0, than the project is acceptable, otherwise must be rejected.
IRR
The internal rate of return of an investment is the discount rate that, when applied to its future cash flows, will produce an NPV of zero. In essence it represents the yield from an investment project. Internal rate of return (IRR) is the annual rate of growth an investment is expected to generate
Selection rule: projects that have an IRR greater than the cost of capital (expressed in the discount rate) are acceptable; the greater the IRR, the more attractive the project.
--------
85% of enterprises are taking decision regarding only the payback time. (Erfahrungswert aus Energieeffizienznetzwerk IREES).

## Slide 41: How to evaluate Non-Energy Benefits?

## Slide 42: Example of indicator
 | Measure evaluated by ?
Reduced malfunction or breakdown of machinery and equipment | 
Increased production volume | 
Improved product quality | 
Reduced hazardous waste | 
Reduced maintenance cost | 
Notes: Instruction to trainer: You can ask participants to reflect on the type of indicator to quantify / monetize one or two of these NEBs

## Slide 43: Example of indicator
 | Measure evaluated by
Reduced malfunction or breakdown of machinery and equipment | Number of malfunction or breakdown
Increased production volume | Increased annual quantity x unit price
Improved product quality | Reduction of material costs due to reduced rejects Number of complaints Number of returns
Reduced hazardous waste | Disposal costs
Reduced maintenance cost | Wages x reduced maintenance hours
Source: Multiple Benefits Webinar 1: Einführung und Überblick in die Mehrfachnutzen-Analyse

## Slide 44: Quantifiability of NEBs
Low
High
Increased production, Reduced operating time, Improved equipment performance, Shorter process cycle times, Reduced operational costs, Reduced amount of raw material
Productivity gains, improved efficiency, improved product quality, increased capacity, improved capacity utilisation, improved temperature control, lowered cooling requirements
Improved worker safety, improved work environment, decreased noise, improved lighting, additional space, reduced need for personal protective equipment, improved air quality
Reduced labour costs, reduced maintenance costs, reduced wear and tear on equipment and machinery, extended life of equipment, reduced scrap/rework costs, improved reliability
Reduced waste and waste costs, reduced emissions, reduced costs of environmental compliance, reduced need for engineering controls delaying or reducing capital expenditures, decreased liability, increased asset values, improved process control
Improved public image, increased job satisfaction, improved worker morale, competitive advantage, improved customer satisfaction, reduced risks (legal, energy price, energy supply, commercial), health benefits
Source: Rasmussen, J (2014). ‘Energy-efficiency investments and the concepts of Non-Energy Benefits and investment behaviour‘
medium
Time
Short term
Long term
Notes: Instruction to trainer: Use this slide to show the different categories that can be made with NEBs: Impact on short/long term and high/medium/low possibility to quantify.
Some NEBs are easy to monetize (increased production, higher productivity, reduced dowtime, reduced waste or wastewater etc.), some of them are easy to quantify but maybe harder to monetize (reduced noise, better air quality, improved staff satisfaction).
Nevertheless, only monetary aspects are not enough to push investment decision and that‘s why it is crucial to list all potential benefits of an Energy Efficiency measure (EEM), even if it‘s not possible to translate them into numbers, to:
find the right interlocutor in the company who could also push the project (financial, technical, management position) and
also to link the EEM with cost reductions/ lower risks / added value to the company core business.
NEBs can affect how decisions are made, which budget it gets paid from, also when it‘s described qualitatively.

## Slide 45: Introduction to the GEAR@SME - Business Case Tool
Notes: Instruction to trainer: You can introduce the Business Case Tool and more specifically the Mbenefits list included. Some indicators are listed to help quantify or monetize NEBs.

## Slide 46: Introduction to the GEAR@SME - Business Tool Case
Help to quantify

## Slide 47: Introduction to the GEAR@SME - Business Tool Case
Help to monetize

## Slide 48: Examples
Notes: Instruction to trainer: Show one or several case studies to illustrate the calculation

## Slide 49: Rooftop solar, heat exchanger to deliver on Supermarket chain’s sustainability ambitions
 | All benefits | Energy-only benefits
Net Present Value | 291.408 € | 18.314 €
Internal rate of return | 17,0% | 10,5%
Simple Payback | 3,6 years | 4,8 years
Example #1
Sector: Retail (warehouse for grocery chain)
Size: 230 employees
Location: Greece
Measure: Install rooftop PV system and heat exchanger
NEBs quantified: increased economic, social and environmental value thoughout the supply chain; avoided regulatory compliance costs; emissions reduction; reduced regulatory risk
Investment duration (NPV, IRR): 10 years
CAPEX: 797.538 € (Rooftop Solar PV)
 | All benefits | Energy-only benefits
Net Present Value | 48.575 € | 29.662 €
Internal rate of return | 28,3% | 21,6%
Simple Payback | 2,8 years | 3,1 years
CAPEX: 58.828 € (Heat exchanger)
Notes: Source: Case Study Mbenefits, available at: https://www.mbenefits.eu/news-resources/library/ (last accessed 9.11.2021)
Introduction
Alfa-Beta (AB) Vassilopoulos S.A. is a supermarket chain based in Greece. Their value proposition is to provide a great shopping experience
that meets consumers’ changing needs and builds loyalty, all provided with 24-hour technical support.
They aim to inspire customers to make healthier choices, increase product transparency, and eliminate waste. Part of AB Vassilopoulo’s
goal is to target smarter and more efficient operations. Given the staff’s time constraints and the fact that an energy audit
was not legally required at the warehouse in focus, participating in the Multiple Benefits project offered a unique opportunity to investigate
energy saving opportunities and additional benefits.
Energy insights -2,2% reduction of energy demand (heat exchanger)

## Slide 50: Complete renovation of an office building
 | All benefits | Energy-only benefits
Investment income before taxes | 3.390.000 CHF | 380.000 CHF
Net Present Value | 4.840.000 CHF | -20.170.000 CHF
Internal rate of return | 11,0% | -11,7%
Simple Payback | 8 years | 49 years
Example #2
Sector: Office building
Size: large company
Location: Switzerland
Measure: Complete renovation
NEBs quantified: better space use; maintenance cost reduction; CO2 cost reduction; reduction of wear & tear of machinery and equipment; reduced cost of complaint management and adjustments; improved employee productivity
Investment duration (NPV, IRR): 15 years
CAPEX: 24.000.000 CHF (approx 22.700.000 €)
Discount rate: 8%
Notes: Instruction to trainer: Only this example contains some hypothesis on how the calculation of the NEBs has been made
Source: Part of the presentation of Beyond Energy Savings: Quantifying the Additional Benefits from Energy Efficiency, from Catherine Cooremans, 12.01.2020, available at : https://www.mbenefits.eu/news-resources/library/ (last accessed 09.11.2021)
With energy-only benefits, the project doesn‘t make sense in financial terms. NPV and IRR are negative. If you add Non-Energy Benefits, the CAPEX is the same, NPV is positive and IRR is 11%. It‘s a long investment duration (15 years) but regarding heavy renovation of a building, so it make sense.
Investment income before taxes: sum of benefits of the measure. Energy only and sum of all non energy benefits.
CO2 cost reduction because there is a CO2 tax in Switzerland.
Hypothesis that the turnover would be reduced by 0,5% because the building is morecomfortable and because of a better image of the company.
There were a lots of complaints before because the building was very old.
Looking at invoices, they could asses all benefits involved in the project.
For the productivity they made a hypothesis of an increase of 1,25% so it's a very conservative hypothesis. They made this hypothesis together with people of the company.
In this example,Non-Energy Benefits figures do not take into account an increased value of the real estate asset or possible increases in energy and CO2 prices.

## Slide 51: Replacement of rectifiers
 | All benefits | Energy-only benefits
Net Present Value | 1.904.476 CHF | 10.489 CHF
Internal rate of return | 118% | 6,9%
Simple Payback | 0,85 years | 6 years
Example #3
Sector: Surface treatment of metal pieces
Size: SME
Location: Switzerland
Measure: replacement of rectifiers (high performance)
NEBs quantified: reduced labour costs (fewer overtime hour, fewer pieces to re-make), reduced cooling water costs, less material waste, higher production capacity
Investment duration (NPV, IRR): 8 years
Discount rate: 6%
Rectifiers obsolete (> 35 years), low performance (50-60%), insufficient capacity which limits the number and size of pieces processed simultaneously, difficult and expensive to repair.
Notes: Source: Metal surface treatment industry example, Mbenefits Case study, available at: https://www.mbenefits.eu/news-resources/library/ (last accessed 09.11.2021)
A rectifier: an electrical device that converts alternating current, which periodically reverses direction, to direct current (DC), which flows in only one direction. The process is known as rectification, since it "straightens" the direction
Situational analysis
• Rectifiers1 obsolete > 35 years
• Low performance (50-60%)
• Insufficient capacity limits number and size of pieces processed simultaneously
• Difficult and expensive to repair
Project description
• Replace rectifiers with high performance electronic models (85-93%)
• Reduced energy consumption
• Cooling system improvement
• More efficient control systemof current. (Source: Wikipedia)
Post-installation
• 10% improvement
• 63,000 kWh annual energy consumption savings

## Slide 52: New batteries with modern chargers to save time, reduce cost at warehouse operation
 | All benefits | Energy-only benefits
Net Present Value | 340.011 € | 11.864 €
Internal rate of return | 20,4 % | 10,4%
Simple Payback | 5,8 years | 9,9 years
Example #4
Sector: Retail (warehouse for grocery chain)
Size: 230 employees
Location: Greece
Measure: Deployment of Li-ion batteries and modern charging station
NEBsquantified: reduced maintenance costs
CAPEX: 700.427 €
Investment duration (NPV, IRR): 10 years
Notes: Source: Case Study Mbenefits, available at: https://www.mbenefits.eu/news-resources/library/ (last accessed 9.11.2021)
Introduction
Alfa-Beta (AB) Vassilopoulos S.A. is a supermarket chain based in Greece. Their value proposition is to provide a great shopping experience that meets consumers’ changing needs and builds loyalty, all provided with 24-hour technical support.
They aim to inspire customers to make healthier choices, increase product transparency, and eliminate waste. Part of AB Vassilopoulo’s goal is to target smarter and more efficient operations. Given the staff’s time constraints and the fact that an energy audit was not legally required at the warehouse in focus, participating in the Multiple Benefits project offered a unique opportunity to investigate energy saving opportunities and additional benefits.
Energy insights -2,6% reduction of energy demand
Audit identified following measures:
• Replace Lead-Acid Batteries with Lithium-Ion Batteries for forklifts
• Replace existing chargers with modern chargers designed to provide fast battery charging.

## Slide 53: Barriers to the inclusion of MB in the evaluation of EEM
Missing data
Interdepartmental communication
Average values difficult to determine
Site-specific factors
Time and ability
Often negative risk assessment of MB
Management and communication deficiency
Negative impact possible
Notes: Source: Multiple Benefits Webinar 1: Einführung und Überblick in die Mehrfachnutzen-Analyse accessible on https://www.youtube.com/watch?v=Rx9_LQqFSR8 (last accessed on 17.11.2020)
Missing data: There are often missing data on the process/equipment level.
Interdepartmental communication: Addressing MB requires communication between different departments, the communication can also fail at this level.
Average values difficult to determine: average values could be used in the quantification of MB, when company specific data are too complicated to gather. However, these average values are difficult to determine.
Site-specific factors: the MB depend not only on the EEM itself but also depends on site-specific factors. The same EEM doesn’t always bring the same benefits.
Time and ability: are necessary to follow the benefits. The data collection is time consuming.
Often negative risk assessment of MB: the investment decision often still depend only from the financial results. The risk assessment of an EEM is not always done, but when it is, the risk assessement is often vague and negative, although many positive impacts or benefits can be evaluated.
Management and communication deficiency: the approach and arguments that energy service supplier / energy people usually use doesn’t correspond to the interests or language from the top-management / people making the decisions. It‘s more efficient to change from the cost/ benefit approach to the strategical approach.
Possible negative impacts: Negative impacts are also possible, which could cancel the identified benefits. These negative impacts can be as difficult to assess as the benefits on the productivity for example. With the change of a new technology, there is a need to form the employees. The maintenance can be more difficult for the company. Or the implementation of a measure can involve a downtime for the production, and a production loss.

## Slide 54: Take-aways
Analysing the process together with energy people and production people lead enables to identify EEMs linked to the core business
An investment can be seen as strategic if it contributes to reduced costs, increased value creation and reduced risk
NEBscan contribute to these three aspects and hence to the strategic value of an EE investment
If an investment does not only provide (energy) cost reductions but can be seen as a strategic investment, it is more likely to be prioritized for implementation
NEBsrelated to the operational excellence are easier to quantify
Notes: If partcipants should take away a few elements from Unit II, it will be …

## Slide 55: Questions & Feedback
Notes: Instruction to trainer: Ask participants if they have questions about the training. Don‘t forget to ask participants for feedback and ask questions for „verification“ purpose. Use the questionnaire for participants in the Template Monitoring Training – Multiple Benefits.

## Slide 56
Thanks for your attention!